FANUC X4.7 Installation

1、Output wiring configuration:

Red Wiring：+24VDC       Black Wiring：0VDC

Green Wiring： X4.7 skip    Yellow：Low Battery Signal

2、Signal Test：

System –PMC -Check the state of X4.7 could be changed to 1 from 0.

3、Test the Skip function:

Turn to the MDI mode and input below words:

G91 G31 X100. F100.;

G91 G01 Y100.F100.;

Press the Cycle Begin button, and watch the when the change of X position number, The G31 movement could be skip when touch the stylus！

4、Install the probe into the CNC axis, and adjust the swing of stylus to less than 0.01MM。

5、Change the parameter：

| 6200 | SKF | SRE |  | HSS |  |  | SK0 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Value | 1 | 0 |  | 1 |  |  | 0 |  |
| 6201 |  |  |  |  |  |  | SEB | SEA |
| Value |  |  |  |  |  |  | 1 | 0 |
| 3708 |  |  |  |  |  |  |  | SAR |
| Value |  |  |  |  |  |  |  | 0 |